RYK-9122 Portable Security Recorder :

MPEG4 compression. Portable and compact size. Video loss auto detection. Audio recording. Adjustable sensitivity and area selectable for motion detection. Three levels image quality. Backup ASF file format with time stamp. Record mode: Manual / Continuous / Motion Detection. Independent frame rate for each recording mode. Support SD card. DC5V or 2xAA Batteries.

Features :

Storage Capacity : Quality Level 704x240@24 IPS 320x240@30 IPS High 64 160 Medium 128 320 Low 192 480 (Approx for recording motion movie with 1GB Card.)

Specifications : Model Name RYK-9122 Video System NTSC / PAL with Video Loss Auto Detection Video Codec MPEG4SP ASF File Format Video Record Frame Rate 704x480@12 IPS,352x240@30 IPS (NTSC), 704x576@10 IPS, 352x280@25 IPS (PAL) Video Record Quality High / Medium / Low Video Recording Date / Time Overlay with Video Images in ASF File Video Input 1 CH, Phone Jack Video Output 1 CH, Phone Jack Audio Sampling Rate 44.1 KHz Audio Codec G.726 / 32 kbps Audio Input 1 CH, Phone Jack Audio Output 1 CH, Phone Jack Storage Media Secure Digital (SD) Card Recording Mode Schedule / Motion Detection / Manual Motion Detection Setting Multiple Blocks and adjustable sensitivity Playback Function Play / Fast Forward / Fast Rewind / Pause / Step Forward / Step Rewind Playback Speed x1 / x2 / x4 / x8 / x16 / x32 Power Supply AC100~240V 50/60 Hz, DC5V / 1A or AAx2 Batteries Rechargeable Ni-MH / Alkaline Battery / CRV3 / RCRV3 Power Consumption 2.5W max. Weight 150 g (without Battery) Dimensions (WxHxD) 65x90x27 mm Operating Environment 30~80% RH, 5°C ~ 40°C (41°F ~ 104°F) *Design and specifications are subject to change without notice.

Meicheng® MEI CHENG AUDIO VIDEO CO., LTD.

Address:13F, No. 2, Jian 8th Rd., Jhonghe City, Taipei County 23511, TAIWAN Tel: +886(2) 8228 0311, Fax: +886(2) 8228 0319 Website: www.meicheng.com.tw Email:mei.cheng@msa.hinet.net

# Text boxes

Meicheng

®

www.meicheng.com.tw

SecuMate Mini Portable Security Recorder  RYK-9122

▼Pack size of cigarette

▼Car camera / recorder

▼AA battery x 2

(3 hrs continuously recording)